## Slide 1: BRX Technical Training
Onboard Analog I/O

## Slide 2: Onboard Analog I/O
BX10
  6 discrete IN (all high-speed)
  4 discrete OUT (2 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX10E
  6 discrete IN (all high-speed)
  4 discrete OUT (2 high-speed)
  1 analog IN
  1 analog OUT
  Ethernet port

## Slide 3: Onboard Analog I/O
BX18
  10 discrete IN (all high-speed)
  8 discrete OUT (4 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX18E
  10 discrete IN (all high-speed)
  8 discrete OUT (4 high-speed)
  1 analog IN
  1 analog OUT
  Ethernet port

## Slide 4: Onboard Analog I/O
BX36
  20 discrete IN (10 high-speed)
  16 discrete OUT (8 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX36E
  20 discrete IN (10 high-speed)
  16 discrete OUT (8 high-speed)
  4 analog IN
  2 analog OUT
  Ethernet port

## Slide 5: Onboard Analog I/O
Each channel fully configurable
  No need to specify characteristics for purchase
Configurable characteristics
  Current VS Voltage
  Voltage Ranges
    0-5VDC, 0-10VDC, ±5VDC, ±10VDC
  mA Ranges
    4-20mA, ±20mA
  Scale WX  RX-memory (real number)
    With or without clamping
  Scale RY-memory (real number)  WY
    With or without clamping

## Slide 6: Onboard Analog I/O
Analog Inputs
New memory type in Do-more: RX0. WX0 always contains the raw count; RX0 the scaled real number.

## Slide 7: Onboard Analog I/O
Analog Outputs
New memory type in Do-more: RY0. WY0 always contains the raw count; RY0 the scaled real number.