## Slide 1: BRX Technical Training
Subroutines

## Slide 2: Subroutines
THE BASICS
  Choose a Subroutine if your application requires…
    An oft-repeated operation of some sort using different set of input/output parameters (e.g. a formula)
  Invoked with a CALL “Call Subroutine” instruction
    Scan branches to the subroutine and returns to the instruction just below the CALL when complete
    The last instruction is always a RET “Return Back to CALL”
  No edge-triggered instructions
  No asynchronous instructions
  No multi-scan instructions
  No Stages
  Has no memory structure members
  Never yields
  Execution order determined by the placement of the CALL instruction

## Slide 3
Project with Programs, Tasks and a Subroutine
  This scan $Main, MyProgram1, MyTask2 & MyProgram2 all execute
  This scan each of them call MySub
  MySub called 4 times in 1 scan
    Thus scan time is extended by the execution time of MySub x 4
Subroutines (Calling)
MyTask1
$Main
MyProgram1
MyTask2
MyTask3
MyProgram2
MySub
MySub

## Slide 4: Subroutines
CALL “Call Subroutine”
  Causes normal ladder scan to branch to Subroutine code
    If Optional Input Parameters are defined, then values in Elements of Input Value column are copied to Elements in Into Subroutine column before branching occurs
    After Subroutine executes & returns, if Optional Output Parameters are defined, then values in Elements of Out of Subroutine column are copied to Elements of Into column
  Code in Subroutine should use Elements named in Into Subroutine & Out of Subroutine columns
----
----

## Slide 5: Subroutines
CALL “Call Subroutine”
  Subroutines are meant to be reused each time with possible different input/output parameters
  If Subroutines already exist & a new CALL instruction is programmed, Do-more Designer will help
    If “No,” then you will have a fresh CALL to define
    If “Yes,” then you can pick which list to use
      Fill in the blanks
  Notice Input Leg
  Notice Counter

## Slide 6: Subroutines
RET “Return Back to CALL”
  Marks the end of a Subroutine
  Automatically inserted when Subroutine is created
  Unconditional output
    No input logic is allowed
    Use RETC “Conditional Return Back to CALL” if needed

## Slide 7: Subroutines
RETC “Conditional Return Back to CALL”
  Ends a Subroutine if the input logic is true
  Conditional output
    At least one Element is required for input logic
    Can be used on multiple rungs
    The RET “Return Back to CALL” is still required to mark the bottom of the Subroutine