## Slide 1: Do-more Technical Training
Documentation

## Slide 2: Documentation
(1) Element Documentation
  Nickname
  Extra Info
  Description
(2) Rung Comments
(3) Title Page
(4) Project Properties Page
(5) *User Document
* Not stored in the PLC

## Slide 3: Documentation
Displaying in Ladder View
  View  Options
  Press <Options> button
  Right-click in Ladder View, select “Options”

## Slide 4: Documentation
Element Documentation (pieces)
  Saved to the disk automatically upon change
  Saved to PLC when “Write PLC” is performed
  Nicknames – alternate name for Element
    1 to 16 characters
    Must begin with alpha-character (“a-z” or “A-Z”) or underscore (“_”)
    All other characters can be alpha-numeric (i.e. including “0-9”) or underscores
    No spaces
    No punctuation
  Extra Info – e.g. panel wiring info, etc.
    1 to 16 characters
    Any character can be alphabet (“a-z” or “A-Z”), numeric (“0-9”), punctuation or arithmetic operator
  Description – e.g. detailed description
    1 to 132 characters
    Any characters same as Extra Info

## Slide 5: Documentation
(1) Element Documentation (edit)
  Tools  Documentation Editor…
  Press <CTRL> + D
  Press <Documentation> button
  Right-click in Ladder View, select “Documentation Editor…”

## Slide 6: Documentation
(1) Element Documentation (columns)
  Element
    Asterisk (*) means:
      Element is used but has no documentation
      Element was used in current edit session
        May or may not exist currently
        Elements not used will disappear when project is closed
      Element is “Unreferenced…”, and only has a Nickname in the project
    Can also be a “Symbolic Const”

## Slide 7: Documentation
(1) Element Documentation (columns)
  Nickname
    For symbolic constants, the Nickname given is shown (e.g. PI)
  Extra Info
    For symbolic constants, it will show the value
  Description
    If longer than column width, line breaks are inserted
    Manual line breaks can be inserted with <CTRL> + <Enter>

## Slide 8: Documentation
(1) Element Documentation (buttons)
  <Add>
    Elements already have a record, so…
    Add is mainly used to create documentation records for Elements not yet existing in Ladder Logic
    Single Record Mode – Enter fields then press <Add Record> button
    Range Mode – creates records for a range of Elements
      Any Elements in the range that already have documentation will not be changed
      Provides a means to create records that can subsequently be edited

## Slide 9: Documentation
(1) Element Documentation (buttons)
  <Symb> – adds a Symbolic Constant not already being used in the Ladder Logic
    Enter the fields & press <Add Record> button
      Notice:
        Constant’s Name shows up in the Nickname field
        Constant’s Value shows up in the Extra Info field

## Slide 10: Documentation
(1) Element Documentation (buttons)
  <Clean> – removes records for Elements & Symbolic Constants that are not currently used in Ladder Logic
    Select Element(s) & press <Delete Selected> button

## Slide 11: Documentation
(1) Element Documentation (buttons)
  <Find> – search Element Documentation records
    Choose Element or Text
    Check Case Sensitivity
    Choose where to search
    Press <OK> button
    <Next> button will now be available
  <Next> - searches for next occurrence

## Slide 12: Documentation
(1) Element Documentation (buttons)
  <Refr> – refresh display
  Sort by:
    Element
      Ascending
      Descending
    Nickname
      Ascending
      Descending
    Data-Block Number/ID – same order as the left column in Memory Configuration
  Default sort option can be set in View  Options  Doc Editor tab

## Slide 13: Documentation
(1) Element Documentation (Cut/Copy/Paste)
  Conventional keys supported:
    Cut – <CTRL> + X
    Copy – <CTRL> + C
    Paste – <CTRL> + V
  Selection:
    Entire row – click on Element
    Individual text – double-click on text
    Range of rows – click & drag on Element
  NOTE: Since Nicknames must be unique, an underscore (“_”) will be prepended & an incremented number (“1”, “2”, “3”, etc.) will be appended to pasted Nicknames
C0 was copied to C1-C9

## Slide 14: Documentation
(1) Element Documentation (Element Browser)
  The Element Documentation Editor is the primary tool for creating/editing Element Documentation
  But Element Browser can be used as well
    Search  Element Browser
    <F9> key
    (1) Enter Source Element, Nickname, Extra Info, Description
    (2) Press <Write Detail> button
    Use <Read Detail> button to reset the test if need be

## Slide 15: Documentation
(2) Rung Comments
  Each Rung can have a text comment
    20 lines of text
    Maximum 2400 characters
    Number of characters/line dependent on font
    Any printable ASCII character
  Tools  Comment Editor
  <CTRL> + K
  Double-clicking in Rung Comment area in Ladder View
  Double-clicking on existing Rung Comment

## Slide 16: Documentation
(2) Rung Comments
  Buttons:
    1st Rung
    Back 5 Rungs
    Back 1 Rung, <PageUp>
    Forward 1 Rung, <PageDown>
    Forward 5 Rungs
    Last Rung
    <Goto…>
    <Move…>
    <Copy…>

## Slide 17: Documentation
(3) Title Page
  Document a general description of entire project & is, by default, the 1st page printed for Project
    20 lines of text
    Maximum 2400 characters
    Number of characters/line dependent on font
    Any printable ASCII character
  Tools  Title Page Editor…
  <CTRL> + T
  <Edit…> in Print, Print All, or Print Preview dialogs

## Slide 18: Documentation
(4) Project Properties Page
  Document information about Project (i.e. version numbers & changes since its creation)
  Displayed on Title Page
  Editor pulled up 1st time Project is saved to disk
  File  Properties

## Slide 19: Documentation
(5) User Document
  Attached to the Project
  Displays as the Start Page
  Any file type that can be displayed in a web browser
  Maximum size: 10 Mbytes
  Not stored in CPU
  Tools  Attach User Document…

## Slide 20: Documentation